## Slide 1: Jumanji: The Case for Dynamic NUCA in the Datacenter
Brian C. Schwedock, Nathan Beckmann
MICRO 2020

## Slide 2: Datacenters care about security and tail latency
Security: data and performance protection among untrusted users (e.g., VMs)
Tail latency: execution time of slowest application requests
Computer systems must be redesigned to efficiently enforce these goals!
Spectre
Meltdown
Front-end query
Back-end requests
Tail latency

## Slide 3: Prior D-NUCAs do not work for datacenter applications!
D-NUCAs improve energy efficiency > 50%!
Problem: After 20 years of research, all D-NUCAs care only about data movement, making them unreliable for datacenter apps
Jumanji is a new D-NUCA that improves security, tail latency, and energy efficiency!
8-core chip multiprocessor (CMP)
Thread
Core
LLC bank
Static NUCA (S-NUCA)
Thread
Core
LLC bank
Dynamic NUCA (D-NUCA)

## Slide 4: High-level overview of Jumanji
VM 3
VM 4
VM 2
VM 1
Lat-crit
Batch
Lat-crit
Lat-crit
Lat-crit
Lat-crit
20-core CMP
Jumanji: places apps’ data in the LLC to meet apps’ high-level goals
Isolates VMs across banks to defend against LLC attacks
2
Reserves space to meet tail-latency deadlines
1
Optimizes batch data placement within each VM
3

## Slide 5: Agenda
Motivation
  Security
  Tail latency
  Prior D-NUCAs
Jumanji’s design
Evaluation
Conclusion

## Slide 6: LLC has a big impact on security and tail latency
LLC banks
20-core CMP
w/ NUCA
LLC banks
20-core CMP
w/ NUCA
Network-on-chip
(NoC) latency
Data movement within the LLC exposes side-channel attacks and determines tail latencies
Many recently discovered side channels occur at the LLC [1]
Larger LLC allocations greatly reduce tail latency [2,3,4]
These works ignore NUCA, and by doing so, miss additional security vulnerabilities and harm efficiency
[1] Liu et al., LLC Side-Channel Attacks, S&P 2015
[2] Chen et al., PARTIES, ASPLOS 2019
[3] Kasture et al., Ubik, ASPLOS 2014
[4] Lo et al., Heracles, ISCA 2015
Thread

## Slide 7: Prior work
D-NUCA: ignoring application goals is harmful
Tail latency: ignoring NUCA wastes cache space
Security: sharing LLC banks is unsafe
Security: sharing LLC banks is unsafe

## Slide 8: Prior LLC designs are insecure and inefficient
Prior LLC designs focus on defending conflict attacks (e.g., prime + probe); way-partitioning is the most common defense
Insecure: Limited LLC associativity prevents defending all processes
Insecure: We demonstrate new port and replacement-policy attacks on prior designs
Wasteful: Ignoring NUCA  lots of unnecessary data movement
Cache controller
Shared cache
contents
1
Imperfect performance
isolation
3
Shared cache ports
2
20-core CMP

## Slide 9: Demonstration: Sharing LLC banks is unsafe
Port attack on Xeon processor LLC
Cache controller
Shared cache
contents
1
Imperfect performance
isolation
3
Shared cache ports
2

## Slide 10: Only prior LLC defense: IRONHIDE
20-core CMP
Secure
Insecure
IRONHIDE is the only prior solution which defends all LLC attacks
It isolates applications across LLC banks, creating two regions: secure and insecure
Although it also defends non-LLC attacks, it only supports one secure region at a time
Additionally, IRONHIDE does not address tail latency and does not minimize data movement as well as D-NUCAs
Omar et al., IRONHIDE, HPCA 2020

## Slide 11: Prior work
D-NUCA: ignoring application goals is harmful
Tail latency: ignoring NUCA wastes cache space
Security: sharing LLC banks is unsafe
Tail latency: ignoring NUCA wastes cache space

## Slide 12: Prior LLC designs for tail latency are inefficient
Prior LLC designs for tail latency dynamically allocate cache space, but ignore NUCA
Wasteful: Ignoring NUCA  lots of unnecessary data movement for latency-critical applications
Wasteful: Latency-critical applications thus need more cache space to meet deadlines, harming co-running batch applications
(And are still insecure)
20-core CMP
Batch
application
Latency-critical
application

## Slide 13: Prior LLC designs for tail latency are inefficient
Latency-critical
application
Batch
application
20-core CMP
Placing data closer lowers avg access latency…
… so less space is needed to maintain tail latency
With S-NUCA, LLC accesses have high latency!
Which leaves more space for co-running batch applications to improve throughput
D-NUCA meets tail-latency deadlines much more efficiently!

## Slide 14: D-NUCA meets deadlines with less LLC space
Simulated 20-core CMP
Running latency-critical application Xapian in isolation
Measured tail latency with different allocation sizes using way-partitioning (S-NUCA) and nearby data placement (D-NUCA)
S-NUCA requires 75% more space!

## Slide 15: Prior work
D-NUCA: ignoring application goals is harmful
Security: sharing LLC banks is unsafe
Tail latency: ignoring NUCA wastes cache space
D-NUCA: ignoring application goals is harmful

## Slide 16: Unfortunately, prior D-NUCAs fail in the datacenter
Dynamic non-uniform cache access (D-NUCA) architectures place data in LLC banks to minimize data movement
… but data movement != security and tail latency
 Jigsaw performs well on throughput-oriented batch applications, but poorly for all other goals
Jigsaw: State-of-the-art D-NUCA
Latency-critical
application
Batch
application
Tail latency for Jigsaw vs Jumanji
Beckmann et al., Jigsaw, PACT 2013

## Slide 17: Jumanji is the solution!
Defends all applications against more LLC attacks
Meets tail-latency deadlines with minimal data movement
Maximizes throughput of co-running batch applications
Simple design and small software changes to Jigsaw

## Slide 18: Agenda
Motivation
  Security
  Tail latency
  Prior D-NUCAs
Jumanji’s design
Evaluation
Conclusion

## Slide 19: Jumanji Software
Jumanji OS Runtime
Jumanji Hardware
VTB (update data placement)
Miss curve monitors
Feedback controller
Request
completes
2
Partition banks among VMs
1
Reserve lat-crit allocation
3
Optimize batch within each VM
Periodically trigger reconfiguration
100 ms
Lat-crit
USER SPACE
…
VM 2
VM 1
Batch

## Slide 20: Step 1: Meeting tail-latency deadlines
Feedback controller
Previous allocation
Tail latency of recent requests
Tail < 85% * deadline
Tail < 95% * deadline
Tail < 105% * deadline
Tail >= 105% * deadline
Decrease by 10%
No change
Increase by 10%
Boost to “safe” size
User-defined deadline
Greedily place data near thread(s)
Periodically trigger reconfiguration
100 ms

## Slide 21: Step 2: Defending LLC attacks
VM 3
VM 4
VM 2
VM 1
Lat-crit
Batch
Lookahead Algo.
Lat-crit
Lat-crit
Lat-crit
Lat-crit
Qureshi et al., UCP, MICRO 2009
Mukkara et al., Whirlpool, ASPLOS 2016
Per-VM miss curves
Merged from each VM’s batch-app curves
Modified to allocate at bank granularity to prevent VMs from sharing banks. This is how Jumanji defends LLC bank attacks.

## Slide 22: Step 3: Optimizing for batch performance
Lat-crit
Lat-crit
Lat-crit
Lat-crit
Lat-crit
Lat-crit
Lat-crit
Lat-crit
Execute Jigsaw on batch apps within each VM
Beckmann et al., Jigsaw, PACT 2013

## Slide 23: Jumanji Hardware (borrowed from Jigsaw)
LLC banks
Out-of-order core
L1d
L1i
TLB
L2
VTB
UMON
LLC bank
VC id
Modified: TLB
Added: VTB, UMON
7
42
VC ids
Placement descriptors
VTB
0
1
0
0
2
2
0
…
0xBEEF  LLC bank 1
Hash
bank id
2
1
2
0
0
1
1
…
VC id: 42
20-core CMP
Addr: 0xBEEF
Beckmann et al., Jigsaw, PACT 2013
Beckmann et al., CDCS, HPCA 2015

## Slide 24: Agenda
Motivation
  Security
  Tail latency
  Prior D-NUCAs
Jumanji’s design
Evaluation
Conclusion

## Slide 25: Evaluation Methodology
Simulate 20-core CMP based on Nehalem using ZSim
20 single-threaded applications split into 4 VMs
Each VM has
  1 latency-critical app (from Tailbench)
  4 batch apps (from SPEC CPU2006)
Latency-critical workloads
  4 copies of the same latency-critical app
  Random mixes of latency-critical apps
Batch workloads
  40 random mixes of batch apps for each latency-critical workload

## Slide 26: Evaluation Methodology – LLC Designs
Adaptive:
Meets deadlines using way-partitioning and feedback controller
VM-Part:
Also way-partitions across VMs to defend conflict attacks (but not our new attacks)
Jigsaw
Jumanji

## Slide 27: Jumanji meets deadlines and speeds up batch apps
Latency-critical apps: Xapian x 4
%

## Slide 28: Jumanji meets deadlines and speeds up batch apps
Latency-critical apps: random mixes from Tailbench
%

## Slide 29: See the paper for more results!
Jumanji’s data placement is nearly ideal
Jumanji scales well with VM size
Also…
  Energy savings
  Security analysis
  System sensitivity study

## Slide 30: Agenda
Motivation
  Security
  Tail latency
  Prior D-NUCAs
Jumanji’s design
Evaluation
Conclusion

## Slide 31: Jumanji makes D-NUCA viable in the datacenter
Jumanji recognizes the advantages D-NUCA provides for security and tail latency
Isolating untrusted VMs across LLC banks provides stronger security than prior designs
Placing latency-critical data near cores saves cache space for co-running batch applications
The overall design makes D-NUCA work for modern application goals
Lat-crit
Lat-crit
Lat-crit
Lat-crit
Brian Schwedock bschwedo@andrew.cmu.edu
Nathan Beckmann beckmann@cs.cmu.edu
This presentation and recording belong to the authors. No distribution is allowed without the authors’ permission.